## Slide 1: PlumeTrace
AI-Powered Municipal Environmental Forensics Platform
Team Name: PlumeTrace
Team Leader Name: SUDARSHAN AJOY SINDHU
Teammates Name: SAURABH KHOLLI
College Name: ABV IIITM GWALIOR

## Slide 2: PROBLEM STATEMENT Municipal agencies detect air quality violations daily, but proving which facility caused a pollution plume remains the critical bottleneck for enforcement action. • Sparse IoT sensor grids capture local concentrations but cannot trace pollutant transport paths through complex urban wind fields. • Manual traceback involving weather lookups, property searches, and legal drafting delays field response by hours or days. • Generic AI alerts lack physical constraints derived from atmospheric transport equations, making source claims legally indefensible. • Compliance evidence must form an unbroken chain from sensor reading → wind vector → predicted source → facility history → regulatory citation. PlumeTrace closes this gap: it converts a critical hazard alert into real-time, physics-backed source attribution and a review-ready regulatory enforcement warning.

## Slide 3: ABSTRACT PlumeTrace is an AI-powered environmental forensics platform for municipal smart-city hazard response, combining physics-informed deep learning with autonomous compliance workflows. • Eight industrial-zone IoT sensors publish live air-quality telemetry (SO₂, PM2.5, wind vectors, altitude) through an MQTT broker at 2-second intervals. • An asynchronous FastAPI backend validates payloads via Pydantic v2, persists to SQLite, and broadcasts readings to the dashboard via Server-Sent Events (SSE). • A 4D Physics-Informed Neural Network (PINN) solves the advection-diffusion PDE ∂C/∂t + u·∇C − D∇²C = 0 backwards in (x, y, z, t) to estimate upstream emission origin. • LangGraph state-machine agents enrich alerts with meteorological vectors, RAG-retrieved Clean Air Act policies, facility registry records, and enforcement language. • A human-in-the-loop review panel allows operators to approve, reject, or request AI-powered refinements to draft enforcement reports before dispatch.

## Slide 4: Backend: FastAPI, gmqtt, async SQLAlchemy (aiosqlite), SQLite, Pydantic v2, SSE Manager with auto-reconnection. Streaming: Embedded amqtt MQTT broker with password authentication; gmqtt async client for sensor subscriptions. AI/ML: PyTorch 4D PINN — Fourier Residual architecture (8 blocks, 128 units), Sobol collocation, AdamW + L-BFGS two-stage optimization, SoftAdapt loss weighting. Agents: LangGraph state-machine, LangChain tool integrations, TF-IDF RAG engine for Clean Air Act and municipal zoning policies, deterministic fallback report templates. Frontend: Next.js 14, Tailwind CSS, react-map-gl (MapLibre GL), SSE with exponential backoff reconnection, Lucide icons, interactive scenario simulator. Tuning: Optuna hyperparameter optimization for PINN architecture search (hidden units, layers, Fourier bands, loss weights).
TECH STACK

## Slide 5: Current air-quality response tools leave a critical gap between pollution detection and legally defensible source attribution. • Fixed monitoring dashboards (e.g., AirNow, PurpleAir) show that pollution occurred, but cannot prove which facility caused it. • Offline Gaussian dispersion studies (AERMOD, CALPUFF) can be accurate, but require hours of manual setup — too slow for real-time incident triage. • Generic ML anomaly detection lacks physical constraints, producing source estimates that are difficult to defend in regulatory proceedings. • Manual property-map cross-referencing creates inconsistent evidence trails and slows enforcement response. PlumeTrace unifies live sensor streams, physics-informed 4D inversion, municipal property records, and RAG-augmented legal drafting into one auditable, real-time workflow.
EXISTING SOLUTIONS & DRAWBACKS

## Slide 6: When a sensor reading exceeds safe limits (SO₂ ≥ 75 ppb or PM2.5 ≥ 35 µg/m³), PlumeTrace executes a five-stage analytical response: 1. Validate telemetry via Pydantic v2 strict schemas and persist the reading to the SQLite event database. 2. Broadcast the hazard alert to all connected dashboard clients via SSE and trigger the LangGraph agent state-machine. 3. Run the 4D PINN inverse solver: evaluate source probability over a spatial grid, fuse with physics-based likelihood, and estimate upstream emission coordinates with uncertainty quantification. 4. Snap predicted coordinates to the nearest municipal facility using wind-aware scoring, then retrieve compliance history and zoning permits. 5. Draft a three-paragraph regulatory enforcement warning using RAG-retrieved Clean Air Act guidelines and present it for human-in-the-loop review.
PROPOSED SOLUTION

## Slide 7: Telemetry path: IoT Sensors → MQTT (city/airquality/+) → FastAPI gmqtt listener → Pydantic v2 validation → SQLite persistence → SSE broadcast → React dashboard. Hazard path: Alert triage → Meteorological vector tool → 4D PINN source-inversion bridge (Fourier Residual + physics-fused posterior) → Municipal property registry search → RAG policy retrieval → Compliance report generation → Human-in-the-loop review panel. The design is fully asynchronous at every boundary: MQTT ingestion, SSE broadcasting, PINN inference (offloaded to thread pool), and LangGraph agent execution run concurrently without blocking the API server. SSE connections feature automatic exponential backoff reconnection (1s → 2s → 4s → max 30s), ensuring the dashboard recovers seamlessly from backend restarts or network interruptions.
ARCHITECTURE / WORKFLOW

## Slide 8: • Neuro-symbolic response loop: deterministic hazard thresholds and municipal registry rules frame AI-generated enforcement text, ensuring legal defensibility. • 4D Physics-informed source attribution: the PINN is constrained by ∂C/∂t + u·∂C/∂x + v·∂C/∂y + w·∂C/∂z − Dh·(∂²C/∂x² + ∂²C/∂y²) − Dv·∂²C/∂z² = 0, incorporating vertical transport and altitude-aware sensing. • Physics-fused Bayesian posterior: PINN neural prior is multiplied by analytic advection-diffusion likelihood to produce calibrated source probability maps with spatial uncertainty quantification. • RAG-augmented legal drafting: enforcement reports are grounded in dynamically retrieved Clean Air Act sections and local municipal zoning codes via TF-IDF vector search. • Human-in-the-loop review: operators can approve, reject, or request AI-powered refinements to draft reports before dispatch — maintaining human oversight over autonomous enforcement.
UNIQUENESS / INNOVATION

## Slide 9: Advantages • Sub-second source attribution during municipal hazard events, replacing hours of manual traceback. • Complete evidence chain: sensor coordinates → wind vectors → AI inference → registry data → regulatory citation → human approval. • Modular architecture: swap SQLite for PostGIS, mock weather for live NOAA APIs, synthetic sensors for real stations. • Robust frontend with automatic SSE reconnection and interactive scenario simulator for operator training. Limitations • Current prototype uses four synthetic sensors and static property records; real deployments require calibration with terrain and boundary-layer data. • PINN inference runs on CPU in the demo; production deployments would benefit from GPU acceleration or ONNX compilation for edge hardware.
ADVANTAGES & LIMITATIONS

## Slide 10: PlumeTrace demonstrates a practical smart-city response loop: detect, attribute, document, and escalate — all within seconds of a hazardous air quality event. The prototype runs end-to-end: MQTT telemetry ingestion → 4D PINN inverse dispersion → LangGraph agent orchestration → RAG-augmented enforcement drafting → human-in-the-loop review — verified with live sensor streams and browser-rendered compliance reports. Next milestones: live NOAA meteorological APIs, multi-pollutant cross-correlation (SO₂ + VOC fingerprinting), ONNX/TensorRT edge compilation, PostGIS spatial database, and a mobile field-verification companion app.
CONCLUSION

## Slide 11: Implemented prototype artifacts • backend/app/main.py, mqtt_handler.py, sse_manager.py, models.py, schemas.py, rag_engine.py, database.py, config.py • pinn_engine.py — 4D Fourier Residual PINN with SoftAdapt adaptive loss weighting and Sobol collocation • agent_orchestrator.py — LangGraph state-machine with 6 nodes: triage, weather, PINN bridge, registry, RAG, report • frontend/src/components/MapEngine.tsx, SidebarLogs.tsx — SSE with exponential backoff, scenario simulator • pinn/config.py, pinn/utils.py, pinn/tune.py — Optuna hyperparameter optimization framework Technical references • FastAPI, gmqtt, amqtt, SQLAlchemy asyncio, PyTorch autograd + Sobol, LangGraph/LangChain, react-map-gl/MapLibre GL, Optuna, Pydantic v2 REFERENCES